## Slide 1
B.ENG. PROJECT PRESENTATION
Fault Detection and Diagnosis in Power System Using Machine Learning Techniques
Dimpka Awajimmama
Matriculation Number: FUO/20/EEE/13132
Department of Electrical and Electronics Engineering
Faculty of Engineering, Federal University Otuoke
Supervised by: [Supervisor's Name]

## Slide 2
CHAPTER ONE
Problem Statement & Objectives
2 / 10
Fault Detection & Diagnosis in Power Systems Using ML
THE PROBLEM
Conventional protection schemes — overcurrent, distance, and differential relaying — rely on fixed thresholds and impedance calculations. They often perform poorly under high-impedance faults, weak-grid conditions, and limited monitoring infrastructure, making rapid and precise fault classification and location difficult to achieve.
AIM
To develop and evaluate a Random Forest-based machine learning system for fault detection and diagnosis in a three-phase power transmission network.
OBJECTIVES
1
Simulate a three-phase transmission network in the time domain
2
Generate voltage/current waveforms for healthy and faulted conditions
3
Inject LG, LL, LLG, and LLL faults at randomised locations & severities
4
Extract physically meaningful features from the fault waveforms
5
Train Random Forest classifiers for fault type and fault location
6
Evaluate via cross-validation, confusion matrices, and noise testing

## Slide 3
CHAPTER TWO
Related Work & Research Gaps
3 / 10
Fault Detection & Diagnosis in Power Systems Using ML
WHAT PRIOR WORK ESTABLISHED
•
Symmetrical components (Fortescue, 1918)
Still the standard analytical tool for characterising fault type from voltage/current signatures.
•
Random Forest (Breiman, 2001)
Ensemble decision trees resist overfitting and combine strong accuracy with interpretability.
•
Mehdi et al. (2020); Fonseca et al. (2022)
RF classifiers using statistical/harmonic signal features achieved strong fault-type accuracy.
•
Mukherjee et al. (2021)
Reviews confirm fault location is consistently harder than fault-type classification.
GAPS THIS STUDY ADDRESSES
Many studies rely on commercial or unverified simulation toolchains — limiting transparency and reproducibility.
Scenario parameters unavailable at inference time (fault resistance, inception angle) are often left in feature sets, risking data leakage and inflated accuracy.
Fault-location estimation receives far less attention than fault-type classification, despite being the harder problem.
Robustness to measurement noise is rarely tested systematically alongside clean-data accuracy.

## Slide 4
CHAPTER THREE
Materials
4 / 10
Fault Detection & Diagnosis in Power Systems Using ML
H
Hardware
Dell Latitude 3150 laptop (single machine used for all work)
Intel Celeron N2840 processor
4 GB RAM
No dedicated graphics processing unit (GPU)
This modest hardware profile was a deliberate constraint — it favoured a computationally lightweight simulation and a classical ensemble classifier (Random Forest) over GPU-hungry deep learning architectures.
S
Software (Python 3)
NumPy — numerical arrays & linear algebra for the state-space simulation
SciPy — supporting numerical routines for simulation development
pandas — dataset assembly, storage, and manipulation
scikit-learn — Random Forest, train/test split, cross-validation, metrics
Matplotlib — waveform plots, confusion matrices, feature-importance charts
joblib — persistence of trained classifier models

## Slide 5
CHAPTER THREE
Method — Network Model & Fault Modelling
5 / 10
Fault Detection & Diagnosis in Power Systems Using ML
NETWORK MODEL
Three-phase source with realistic Thevenin resistance & reactance (needed for voltage sag to appear during faults)
Transmission line divided into 6 series-connected sections, each with coupled self/mutual impedance and shunt capacitance
Balanced three-phase resistive-inductive (RL) load
Solved as a state-space system using an A-stable implicit backward-Euler / trapezoidal integrator
Parameter | Value
Line-to-line RMS voltage | 11 kV
Frequency | 50 Hz
Line sections | 6
Sampling frequency | 10 kHz
Fault-clearing transition | 0.02 s (20 ms)
FAULT MODELLING & INJECTION
LG
Single line-to-ground: one phase to ground
LL
Line-to-line: two phases tied together
LLG
Double line-to-ground: two phases + ground
LLL
Three-phase: all phases tied together

## Slide 6
CHAPTER THREE
Method — Scenario Generation & Feature Extraction
6 / 10
Fault Detection & Diagnosis in Power Systems Using ML
SIMULATION SCENARIOS
3,000
total simulation runs
5
balanced classes
(Normal, LG, LL, LLG, LLL)
600
runs per class
Randomised per run: fault type, faulted phase(s), fault section (1–6), fault resistance (0–100 Ω), inception angle (0°–180°), fault duration (0.05–0.3 s), small load variation.
FEATURE EXTRACTION — 51 FEATURES PER RUN
36
Time-domain statistics — RMS, mean, std dev, skewness, kurtosis, peak-to-peak across Va, Vb, Vc, Ia, Ib, Ic
6
Symmetrical component magnitudes — Positive-, negative-, zero-sequence RMS for voltage & current
2
Sequence ratios — V2/V1 and V0/V1
7
Apparent impedance features — Magnitude & angle per phase, plus positive-sequence magnitude

## Slide 7
CHAPTER THREE
Method — Model Development & Evaluation
7 / 10
Fault Detection & Diagnosis in Power Systems Using ML
TWO RANDOM FOREST CLASSIFIERS
scikit-learn implementation · 200 estimators · fixed random seed · 70% train / 30% held-out test split
Fault-Type Classifier
5 classes (Normal, LG, LL, LLG, LLL) — trained on all 3,000 runs
Fault-Location Classifier
6 line sections — trained on the 2,400 fault-containing runs only
EVALUATION METHODOLOGY
5-fold stratified cross-validation (mean ± standard deviation)
Full confusion matrices and per-class precision, recall, F1-score
Random Forest feature-importance ranking (mean decrease in impurity)
Noise-robustness testing: Gaussian measurement noise added at 40 dB, 30 dB, and 20 dB SNR before feature re-extraction

## Slide 8
CHAPTER FOUR
Results — Fault-Type Classifier
8 / 10
Fault Detection & Diagnosis in Power Systems Using ML
100%
held-out test accuracy
(900 / 900 correct)
99.90%
± 0.19% — 5-fold
cross-validation accuracy
Top features
Zero- and negative-sequence voltage/current dominate — the model rediscovered classical symmetrical-component theory.
NOISE ROBUSTNESS
Chart: 
| Clean | 40 dB | 30 dB | 20 dB
Test Accuracy (%) | 100 | 100 | 97.1 | 72.9

## Slide 9
CHAPTER FOUR
Results — Fault-Location Classifier & Discussion
9 / 10
Fault Detection & Diagnosis in Power Systems Using ML
EFFECT OF APPARENT IMPEDANCE FEATURES
Chart: 
| 44 features (time + sequence) | 51 features (+ impedance)
Test Accuracy (%) | 55.3 | 62.8
5-fold CV accuracy improved similarly: 52.4% ± 2.0% → 58.6% ± 2.8%. Of 268 remaining errors, 67% were between physically adjacent line sections.
DISCUSSION
The 100% vs. 62.8% accuracy gap confirms the literature: fault-type classification is a mature, well-solved problem; fault location from single-ended measurement is not.
Fault-type accuracy degrades gracefully under noise (100% → 72.9% at 20 dB SNR) — not a fragile result.
The dataset is noiseless at simulation; noise was tested only afterward as a robustness check, not built into training.

## Slide 10
CHAPTER FIVE
Conclusion
Developed and evaluated a Random Forest-based fault detection and diagnosis system for a three-phase power transmission network, built on a custom Python time-domain simulation and a 51-feature, physically-grounded feature set.
The fault-type classifier achieved 100% test accuracy (99.90% ± 0.19% cross-validation) and degraded gracefully under simulated measurement noise, with feature importance confirming physically interpretable, symmetrical-component-consistent behaviour.
The fault-location classifier achieved a comparatively modest 62.8% test accuracy — confirming that precise fault localisation from a single sending-end measurement point remains a substantially harder problem than fault-type classification, consistent with the broader literature.
10 / 10